## Slide 1
Victoria Manfredi, Ram Ramanathan, Will Tetteh, Regina Hain, Dorene Ryder
August 6, 2017
SHARE: Scalable Hybrid Adaptive Routing for dynamic multi-hop Environments

## Slide 2: Roadmap
Motivation
SHARE protocol
Evaluation
Summary

## Slide 3: Roadmap
Motivation
SHARE protocol
Evaluation
Summary

## Slide 4: 20-50 Billion Wireless Devices by 2020 (Ericsson)
New applications across diverse networks
  p2p cellphone apps
    anonymous chat: bleep, briar, FireChat
  smart vehicle/health/environ monitoring
    Cambridge Mobile Telematics, splitsecnd
  internet access
    Google’s Project Loon
  sharing computational power
    microclouds and cloudlet
Shorter communication ranges
  low power devices such as IoT
  higher data rates: higher frequency bands
Rufus Labs
Google
Parrot
Parrot
Google
Notes: New applications appearing
  higher frequency bands : (e.g. mmWave)

## Slide 5: 20-50 Billion Wireless Devices by 2020 (Ericsson)
New applications across diverse networks
  p2p cellphone apps
    anonymous chat: bleep, briar, FireChat
  smart vehicle/health/environ monitoring
    Cambridge Mobile Telematics, splitsecnd
  internet access
    Google’s Project Loon
  sharing computational power
    microclouds and cloudlet
Shorter communication ranges
  low power devices such as IoT
  higher data rates: higher frequency bands
Rufus Labs
Google
Parrot
Parrot
Google
Many devices + short ranges + multiple networks ⇒ Scalable multi-hop routing protocol
Notes: New applications appearing
  higher frequency bands : (e.g. mmWave)

## Slide 6: Data traffic issues in real-world wireless networks
Traffic falls off with hop-distance
  [Ramanathan et al, 2010]
  local traffic >> non-local traffic
Cost of route setup
  local route << non-local route
Non-local destinations are often sinks
  sensor networks, access points
  many to one traffic
Network dynamics
  mobility, congestion, wireless interference
  path breaks increase with distance to destination
6
Proactively maintain local link state
Reactively build network-wide gradient
Flood when no link or gradient state found
Maintain multiple paths to a destination
Design insights
Notes: Data traffic determines routing state needed
  Redundant transmissions are valuable
Key ideas
  Data traffic patterns should determine routing state needed
    network traffic falls off with hop-distance so most traffic is local
      proactively maintain local link state
    non-local traffic often destined to a sink + topology changes are more costly for non-local destinations
      worthwhile to have multiple paths to non-local destination as in a gradient
  Permit redundant transmissions
    wireless multi-hop networks are inherently dynamic
    provide robustness against topology changes and path breaks that are more likely as distance to destination increases
    flooding
    braiding
wireless multi-hop networks are inherently dynamic
Node density and link breakages in a network change temporally and spatially.
Traffic traveling through a high mobility region of a network is more likely to get dropped than traffic traveling through a low mobility region.
Traffic traveling many hops to a destination is more likely to get dropped than traffic traveling just a few hops.
Traffic traveling through a highly congested region of a network is more likely to get dropped than traffic traveling through a a lightly loaded region.

## Slide 7: Data traffic issues in real-world wireless networks
Traffic falls off with hop-distance
  [Ramanathan et al, 2010]
  local traffic >> non-local traffic
Cost of route setup
  local route << non-local route
Non-local destinations are often sinks
  sensor networks, access points
  many to one traffic
Network dynamics
  mobility, congestion, wireless interference
  path breaks increase with distance to destination
7
Proactively maintain local link state
Reactively build network-wide gradient
Flood when no link or gradient state found
Maintain multiple paths to a destination
Design insights
Notes: Data traffic determines routing state needed
  Redundant transmissions are valuable
Key ideas
  Data traffic patterns should determine routing state needed
    network traffic falls off with hop-distance so most traffic is local
      proactively maintain local link state
    non-local traffic often destined to a sink + topology changes are more costly for non-local destinations
      worthwhile to have multiple paths to non-local destination as in a gradient
  Permit redundant transmissions
    wireless multi-hop networks are inherently dynamic
    provide robustness against topology changes and path breaks that are more likely as distance to destination increases
    flooding
    braiding
wireless multi-hop networks are inherently dynamic
Node density and link breakages in a network change temporally and spatially.
Traffic traveling through a high mobility region of a network is more likely to get dropped than traffic traveling through a low mobility region.
Traffic traveling many hops to a destination is more likely to get dropped than traffic traveling just a few hops.
Traffic traveling through a highly congested region of a network is more likely to get dropped than traffic traveling through a a lightly loaded region.

## Slide 8: Data traffic issues in real-world wireless networks
Traffic falls off with hop-distance
  [Ramanathan et al, 2010]
  local traffic >> non-local traffic
Cost of route setup
  local route << non-local route
Non-local destinations are often sinks
  sensor networks, access points
  many to one traffic
Network dynamics
  mobility, congestion, wireless interference
  path breaks increase with distance to destination
8
Proactively maintain local link state
Reactively build network-wide gradient
Flood when no link or gradient state found
Maintain multiple paths to a destination
Design insights
Notes: Data traffic determines routing state needed
  Redundant transmissions are valuable
Key ideas
  Data traffic patterns should determine routing state needed
    network traffic falls off with hop-distance so most traffic is local
      proactively maintain local link state
    non-local traffic often destined to a sink + topology changes are more costly for non-local destinations
      worthwhile to have multiple paths to non-local destination as in a gradient
  Permit redundant transmissions
    wireless multi-hop networks are inherently dynamic
    provide robustness against topology changes and path breaks that are more likely as distance to destination increases
    flooding
    braiding
wireless multi-hop networks are inherently dynamic
Node density and link breakages in a network change temporally and spatially.
Traffic traveling through a high mobility region of a network is more likely to get dropped than traffic traveling through a low mobility region.
Traffic traveling many hops to a destination is more likely to get dropped than traffic traveling just a few hops.
Traffic traveling through a highly congested region of a network is more likely to get dropped than traffic traveling through a a lightly loaded region.

## Slide 9: Roadmap
Motivation
SHARE protocol
Evaluation
Summary

## Slide 10: SHARE
Scalable Hybrid Adaptive Routing for dynamic multi-hop Environments
  new approach to scalable multi-hop routing
Key components
  Proactive link state routing
    local traffic: < 2 hops
  Reactive gradient routing
    non-local traffic: > 2 hops
    probabilistically truncate gradient control traffic to reduce overhead
  Replication of data packets (“braiding”)
    for robustness against topology changes
  Flooding (only as long as necessary)
    when no gradient or link state found

## Slide 11: SHARE
Scalable Hybrid Adaptive Routing for dynamic multi-hop Environments
  new approach to scalable multi-hop routing
Key components
  Proactive link state routing
    local traffic: < 2 hops
  Reactive gradient routing
    non-local traffic: > 2 hops
    probabilistically truncate gradient control traffic to reduce overhead
  Replication of data packets (“braiding”)
    for robustness against topology changes
  Flooding (only as long as necessary)
    when no gradient or link state found

## Slide 12: Reactive gradient routing
On-demand network wide gradient
  for packets with non-local destinations
  gradient gives cost to destination
    e.g., hop count
  reduces need for state correctness
  provides ready-made backup routes
Components
  Gradient establishment
    should be built rarely since non-local traffic should be rare
  Gradient seeking
    flood packet until link state, gradient state, or destination found
4
3
1
2
2
2
3
3
4
4
4
2
2
3
3
3
3
4
4
4
5
5
5
4
Destination
Source
1

## Slide 13: Reactive gradient routing
On-demand network wide gradient
  for packets with non-local destinations
  gradient gives cost to destination
    e.g., hop count
  reduces need for state correctness
  provides ready-made backup routes
Components
  Gradient establishment
    should be built rarely since non-local traffic should be rare
  Gradient seeking
    flood packet until link state, gradient state, or destination found
4
3
1
2
2
2
3
3
4
4
4
2
2
3
3
3
3
4
4
4
5
5
5
4
Destination
Source
1

## Slide 14: Gradient establishment
GEM
  Gradient Establishment Message
  contains hop count, time generated
  destination triggers GEM generation
Recipients of GEM
  record and increment hop-count
  re-broadcast if most recent timestamp for destination and lowest hop-count
Further limit GEMs generated
  adaptive GEM generation rates
    higher rate if node receiving traffic destined to it
  truncate scope of GEM flood
    probabilistic, density-adaptive approach
4
3
1
2
2
2
3
3
4
4
4
2
2
3
3
3
3
4
4
4
5
5
5
4
Destination
Source
1
Notes: Adaptive GEM sending rate
  low background rate at which all nodes send GEMs
  higher “normal” rate that is triggered as long as a node receives data packets destined for itself and the source of the data packet is not in the destination’s 2-hop link state. A node reduces its GEM rate when it has received no data traffic destined to itself for a threshold period of time.

## Slide 15: Gradient establishment
GEM
  Gradient Establishment Message
  contains hop count, time generated
  destination triggers GEM generation
Recipients of GEM
  record and increment hop-count
  re-broadcast if most recent timestamp for destination and lowest hop-count
Further limit GEMs generated
  adaptive GEM generation rates
    higher rate if node receiving traffic destined to it
  truncate scope of GEM flood
    probabilistic, density-adaptive approach
4
3
1
2
2
2
3
3
4
4
4
2
2
3
3
3
3
4
4
4
5
5
5
4
Destination
Source
1
Notes: Adaptive GEM sending rate
  low background rate at which all nodes send GEMs
  higher “normal” rate that is triggered as long as a node receives data packets destined for itself and the source of the data packet is not in the destination’s 2-hop link state. A node reduces its GEM rate when it has received no data traffic destined to itself for a threshold period of time.

## Slide 16: Truncating the flood of GEMs
Node w broadcasts GEM
Node v determines whether to retransmit
  v wants its ui neighbors to each receive C GEMs
    for gradient path diversity
  v uses local link state to compute retransmission probability
u1 u2 u3 u4
w
v x1 x2 x3
GEM
GEM
Notes:   Node v retransmits a GEM based on the number of w’s 1-hop neighbors that cover each of v’s 1-hop neighbors, excluding w.
  ⇒ w’s 1-hop neighbors excluding v that cover u
  if a node receives a broadcast packet, it knows which of its neighbors should also have received the packet
  C : desired number of nodes “covering” a 1-hop neighbor
  C controls extent to which a packet is flooded
node computes minimum probability, p, that any 1-hop neighbor receives GEM if it does not retransmit
p is computed from link state : each node knows its 1- hop and 2-hop neighborhoods.
Our retransmission must cater to the node that is least covered by nodes with the packet from w.
  Set of forwarders is controlled so that every node gets GEM from sufficient (e.g. 3 to 4) neighbors so that they have some alternate paths, but not from every neighbor
  By probabilistically truncating GEM floods, SHARE intelligently reduces the effective degree of the network thereby reducing the bandwidth incurred by flooded messages.
Scoping GEM floods has the effect of controlling the number of alternate paths of which a node is aware. However, the probabilistic nature of the retransmissions ensures that from one GEM flood to the next, different nodes will probabilistically respond, ensuring in expectation that over multiple floods that all available alternate paths will be found.
The case C ≥ |Cmin| might occur because there are insufficient nodes to cover the 1-hop neighbor, or because the link-state tables have not yet converged or are out of date. Regardless, the correct behavior is still to retransmit the GEM with pR(v) = 1.

## Slide 17: Truncating the flood of GEMs
Node w broadcasts GEM
Node v determines whether to retransmit
  v wants its ui neighbors to each receive C GEMs
    for gradient path diversity
  v uses local link state to compute retransmission probability
u1 u2 u3 u4
w
v x1 x2 x3
GEM
GEM
C1=2 C2=1 C3=1 C4=2
v retransmits with probability
        1 if C ≥ Cmin
      C / Cmin otherwise
Ci : # of GEMs each ui receives if v does not retransmit
Cmin : smallest Ci
Notes:   Node v retransmits a GEM based on the number of w’s 1-hop neighbors that cover each of v’s 1-hop neighbors, excluding w.
  ⇒ w’s 1-hop neighbors excluding v that cover u
  if a node receives a broadcast packet, it knows which of its neighbors should also have received the packet
  C : desired number of nodes “covering” a 1-hop neighbor
  C controls extent to which a packet is flooded
node computes minimum probability, p, that any 1-hop neighbor receives GEM if it does not retransmit
p is computed from link state : each node knows its 1- hop and 2-hop neighborhoods.
Our retransmission must cater to the node that is least covered by nodes with the packet from w.
  Set of forwarders is controlled so that every node gets GEM from sufficient (e.g. 3 to 4) neighbors so that they have some alternate paths, but not from every neighbor
  By probabilistically truncating GEM floods, SHARE intelligently reduces the effective degree of the network thereby reducing the bandwidth incurred by flooded messages.
Scoping GEM floods has the effect of controlling the number of alternate paths of which a node is aware. However, the probabilistic nature of the retransmissions ensures that from one GEM flood to the next, different nodes will probabilistically respond, ensuring in expectation that over multiple floods that all available alternate paths will be found.
The case C ≥ |Cmin| might occur because there are insufficient nodes to cover the 1-hop neighbor, or because the link-state tables have not yet converged or are out of date. Regardless, the correct behavior is still to retransmit the GEM with pR(v) = 1.

## Slide 18: How SHARE nodes forward a packet
Decision loop:
  Step 1. Check link state table
    if destination present, use specified next hop
  Step 2. Check gradient table
    if destination present, use specified next hop
    for additional redundancy, replicate (“braid”) data packets
  Step 3. Flood (only as long as necessary)
    if destination not in link state or gradient table, or TTL=0
    once state is found, flooded packet switches to unicast
    triggers GEMs: future packets should use gradient state
4
3
1
2
2
1
2
3
3
4
2
2
3
3
3
3
∞
∞
∞
∞
Destination
Source
Notes: What happens if the network is partitioned with source and dest in different partitions. The source will keep on flooding. A simple fix is to time out on floods if we don't get gradient or link-state soon...
after a flood, the destination will immediately generate a GEM and switchover to fast GEMs so that very few floods should happen.
Benefits
  fallback mechanism when no link or gradient state for destination
  enables mechanism for network wide broadcast
  allows new nodes to easily join network and start forwarding data
  provides redundancy for important transmissions when desired

## Slide 19: Roadmap
Motivation
SHARE protocol
Evaluation
Summary

## Slide 20: Evaluation
Implemented using ns-3.22 DCE framework
  same network-layer code can directly run on hardware
  very high fidelity limits size of networks to ~70 nodes
  802.11 with RangePropagation of R = 630 m
Scenarios
  √N×√N Stationary Grid
    each grid square is R × R
  Gauss-Markov mobility
    BonnMotion to generate traces, ignore first 3600 s
    nodes distributed within M × M area
    M = N R 2π / D where N is # of nodes and D = 10 is node density
Traffic patterns
  many-to-one: representative of target applications like IoT and 5G
Notes:   Following previous work: packet size is 64 bytes
  simulations length180 s long, traffic starts at 30 seconds and ends at 150 seconds.
  Our simulation sizes are also limited due to the amount of traffic in the network: every node in the network communicates with at least one other node, resulting in correspondingly more flows as the network size increases.
  Traces let SHARE and OLSR operate on same topology
Rangepropagation ensures that for the grid, the topology really conforms to a grid.

## Slide 21: Overhead
Static grid
Gauss Markov, 60 nodes
SHARE overhead grows much more slowly than OLSR overhead as network size increases
SHARE is much more scalable than OLSR
7x more overhead than SHARE
Overhead of both protocols insensitive to speed when # of nodes is fixed
(m/s)

## Slide 22: Delivery ratio
For both static and mobile scenarios:
SHARE has higher delivery ratio than OLSR
Static grid
Gauss Markov
23% more traffic
17% more traffic
Notes: Increasing destinations measures the penalty of gradient control messages, which are proportional to the number of destinations.
Poor connectivity to destination

## Slide 23: Delivery ratio
As traffic gets close to all to all,
SHARE and OLSR converge
Static grid
Gauss Markov
Chart: 49 Nodes, 5 pps / d / node
| 1.0 | 2.0 | 4.0 | 8.0 | 16.0 | 32.0
SHARE | 98 | 99 | 98 | 98 | 94 | 89
OLSR | 93 | 95 | 93 | 92 | 91 | 89
Chart: Traffic rate: 5 pps/node
| 3.0 | 5.0 | 7.0 | 9.0 | 11.0 | 13.0 | 15.0 | 17.0 | 19.0
SHARE | 93 | 88 | 85 | 86 | 80 | 83 | 81 | 81 | 82
OLSR | 82 | 78 | 71 | 73 | 67 | 70 | 63 | 63 | 64
With mobility, OLSR performs significantly worse
Notes: Increasing destinations measures the penalty of gradient control messages, which are proportional to the number of destinations.
Poor connectivity to destination

## Slide 24: Roadmap
Motivation
SHARE protocol
Evaluation
Summary

## Slide 25: SHARE summary
Scalable multi-hop routing unifying several ideas
  proactive link state routing for local traffic
  reactive gradient routing for non-local traffic
  probabilistic truncation of GEM floods to reduce control overhead
  replication of data packets for robustness against topology changes
  flooding when no gradient or link state is found
Compared with OLSR on static and mobile topologies
  SHARE delivers up to 31% more traffic using up to 7x less overhead
Future directions
  further reduce overhead: link state messages, flood scoping, braiding
  generalize to include delay tolerant forwarding
Thank you! Questions? vumanfredi@wesleyan.edu

## Slide 26: References
[Ramanathan et al, 2010]
  R. Ramanathan, R. Allan, P. Basu, J. Feinberg, G. Jakllari, V. Kawadia, S. Loos, J. Redi, C. Santivanez, and J. Freebersyser, “Scalability of mobile ad hoc networks: Theory vs practice,” in Military Communications Conference, 2010-MILCOM 2010. IEEE, 2010, pp. 493–498.

## Slide 27: Proactive link state routing
Maintain 2-hop link state
  use to route data packets with local destinations
  limited control due to 2 hop scope
  robustness benefits from alternative paths
  also use to scope gradient control floods
Components
  Heartbeat messages
    transmitted exactly once
    contain complete neighbor list for a node
  Dijkstra’s algorithm
    nodes use neighbor lists to compute all-pairs for neighborhood
Notes: Most traffic is local: likely be routed using the local link state and only a small portion of the data traffic would be routed using the non-local gradient state

## Slide 28: Braiding
A form of scoped flooding
  replicate data packets over “‘braid” around shortest path
Braid
  subgraph that includes shortest path between source and destination and all nodes and links within k-hops of shortest path
Link state and gradient state make braiding straightforward
  nodes are already aware of alternative paths
  if truncated GEM flood is too restrictive, too few paths to braid well
Packet time-to-live (TTL) constrains flood of braid packets
  set initial packet TTL to maximum desired path length
  node only forwards pkt if path length to dest. < pkt’s current TTL
  generates at most k·TTLMax packets
    packet transmissions form a binary tree of height TTLMax

## Slide 29: Flooding
When no state found, flood data packet
Benefits
  fallback mechanism when no route to destination known
  enables mechanism for network wide broadcast
  allows new nodes to easily join network and start forwarding data
  provides redundancy for important transmissions when desired
Flood only as long as necessary
  stop when packet reaches node with gradient or link state, or reaches destination
Scope using a TTL value that determines number of hops broadcast packet may travel before being dropped
Notes: To accommodate instabilities in the network topology, both the link state and the gradient state provide alternative routes for data traffic, allowing SHARE to deliver data traffic even when the network topology is dynamic.
To provide additional redundancy for forwarding of data packets in dynamic networks, or when there is some potentially out-of-date state, SHARE uses scoped flooding of data packets over a braid around the shortest path on a per- flow basis [18], [14], [34], [20]. How wide to scope the braid is a configurable variable. In the absence of any link state or gradient state, such as in a highly dynamic network, SHARE seamlessly defaults to flooding of data packets, ensuring that traffic is delivered even when no routes exist. This flood, however, is not unconstrained: data packets are only flooded until they reach a node that contains gradient state or link state, or they reach the destination.